## Slide 1: MSR6 TE Requirements USA Operators Domestic Use Cases
Gyan Mishra
Verizon Inc.
July 26th 2022

## Slide 2: Video Transport Use Cases – Bandwidth/Format
Contribution
(External)
Secondary Distribution
Primary Distribution
Studio to Studio
Uncompressed/Lossless Compression
SD: 270 Mbps
HD: 1.5 – 3 Gbps
UHD: 12 Gbps
P-to-P, MP-to-P, P-to-MP
Owner to Provider
- Compressed (Very High quality)
SD: 10-50 Mbps
- HD: 50-100 Mbps
P-to-P and P-to-MP
P-to-MP for DTT/DVB-T
Static Receivers
Provider to Subscriber
- Compressed (MP4 etc.)
Dynamic Receivers
SD: 2 – 6 Mbps
HD: 6 – 16 Mbps
P-to-P for VoD
P-to-MP for IPTV
In all cases, point-to-point + multipoint services over Network Transport are required
Stricter Requirements, Higher per-flow bandwidth
RSVP-TE
(CN)
(AN)
FBB
mLDP
RSVP-TE

## Slide 3: Video Content Delivery Service Providers
Video Stream Bandwidth
Studio to Studio; Broadcaster to Broadcaster (External)
Uncompressed, Lossless
Very High bit-rate stream: SD (270Mbps), HD (1.5-3Gbps)
P-to-P and P2MP (unicast and multicast)
P2MP RSVP-TE
Broadcasters, Studios
Content owner to provider Compressed
Low/moderate bit-rate stream
~ same as secondary dist
P2MP (multicast)
P2MP RSVP-TE
Provider to subscriber i.e.
Cable TV & IPTV
Compressed
Low bit-rate stream: SD (3- 4Mbps mpeg2, 2-3Mbps mpeg4), HD (16-20Mbps mpeg2, 8-10Mpbs mpeg4)
Contribution providers Cable backbones providers
P-to-P for VOD (unicast) & P2MP for IPTV (multicast)
MPLS mLDP
Service Providers
Contribution
Primary Distribution
Secondary Distribution
# of end points

## Slide 4: Video Service Providers Mapping to Broadcast Industry
Contribution
Studio
Studio
Final Studio
Primary Distribution
Common core network requirements & designs
Increasing demand for localised content
Service Control & Broadcast Quality gaining prominence
Increasing scale to end- customer
Mobile Studio
Fixed
Secondary Distribution
RSVP-TE
RSVP-TE
Home Network
Studio
mLDP
Access
VOD
content distributing to scale
DCM
DCM
Network
Super Head End (x2)
VOD
Home x millions
VSO (x100s)
VOD
VOD
DCM / VQE
Head End (x10s)
Local Content Insertion
National Content Insertion
International & National Content
Insertion
Super Head End (x2)

## Slide 5
Public Internet MPLS Network Routing Architecture - USA Domestic Operators - IPv4 Multicast

## Slide 6
Private MPLS Network Routing Architecture – USA Domestic Operators - IPv4 Multicast

## Slide 7: MSR6 Requirements for IPTV Video Delivery transports
Model | QoE | BW Usage per stream (Y) Where X = MPEG stream bw, Z = FEC o/h, and W = FEC + TR overhead, (W < Z) |  | Network Complexity | Video End System Complexity | Delay impact
Fast Convergence | Lossy; target < 1 GOP | Working case: Failure case: | Y = X Y = X | Low | Low | Zero
MPLS TE FRR | Lossy; < 1 GOP | Working case: Failure case: | Y = X Y =>2X | Medium | Low | Zero
MoFRR | Lossy; < 1 GOP | Working case: Failure case: | Y = X Y = X | Low | Low | Zero
FC + FEC or MPLS TE FRR + FEC | Lossless | Working case: Failure case: Fast convergence: FRR: | Y = X * Z Y = X * Z Y =>2X * Z | Fast convergence: Low Fast reroute: Medium | Medium | High
FC + TR or MPLS TE FRR + TR | Lossless | Working case: Failure case: Fast convergence: FRR: | Y =2X Y = X Y =>2X | Fast convergence: Low Fast reroute: Medium | Medium | High
MoFRR + SR | Lossless | Working case: Failure case: | Y = X Y = X | Low | Medium | Low
MPLS TE + SR | Lossless | Working case: Failure case: | Y = X Y = X | High | Medium | Low
MTR + SR MTRISIS MT | Lossless | Working case: Failure case: | Y = X Y = X | High | Medium | Low

## Slide 8: MSR6 Requirements & legacy technologies characteristics to meet?
Characteristic | IP Multicast | MPLS Multicast: RSVP TE | MPLS Multicast: mLDP
Convergence | < ~500ms (< 50ms with MoFRR path separation) | ~50ms (FRR) | < ~500ms (~50ms with p2p MPLS LP)
Offload routing |  (IGP metric based traffic engineering) |  |  (IGP metric based traffic engineering)
Path separation | (MoFRR) |  | (MoFRR)
Admission control and bw reservation | (RSVP) |  | 
Scalable mp2mp |  |  | 
Initiator | Receiver | Source | Receiver
Application | Ideal for single-source multicasts with many leafs | Ideal for single-source multicasts with few leafs | Ideal for dynamic, receiver-driven multicasts with many leafs
Insertion | Secondary Distribution | Contribution | Enterprise VPN

## Slide 9: MSR6 Requirements for Network infrastructure Protection & Resiliency
Preferred choice of transport:
IP (native multicast/PIM) or MPLS (mLDP and RSVP-TE P2MP)
Path selection
(dual path) – MoFRR or exposed to service Tree cost optimization
Load-splitting:
ECMP: PIM and mLDP
Arbitrary: RSVP-TE (CSPF)  Required for Triple Play Services
Preferred choice of virtualization
L2VPN, L3VPN context – or why not…
…not complete list

## Slide 10: MSR6 requirements compare to PIM/mLDP benefits over RSVP-TE P2MP
Cost of trees (in node/network)
N = # tailend LSR (#PE)
PIM/mLDP P2MP: ~1, RSVP-TE P2MP: ~N
Full mesh of RSVP-TE P2MP LSP: ~(N * N) Bidir-PIM/mLDP MP2MP: ~1
Summary: No scaling impact of N for PIM/mLDP
Locality:
Affects convergence/reoptimization speed:
PIM/mLDP: Failure in network affects only router in region (eg: in pink region).
RSVP: impact headend and all affected midpoint and tailends for RSVP-TE reoptimization.
Join/leave of members affect only routers up to first router on the tree in mLDP/PIM. Will affect headend and all midpoints in RSVP-TE P2MP.
Src
Rcv
Rcv
Rcv
Headend LSR

## Slide 11: MSR6 Requirements compare to RSVP-TE P2MP benefits over PIM/mLDP
Sub 50 msec protection
Load-split traffic across alternative paths (ECMP or not)
PIM/mLDP tree follows shortest path, “dense” receiver population == dense use of links
RSVP-TE P2MP ERO trees (RED/PINK) under control of headend LSR.
CSPF load split based on available bandwidth. “Steiner tree” CSPF modifications possible
Block (stop) trees on redundancy loss
Assume high-prio and low-prio trees.
With full redundancy, enough bandwidth to carry all trees (with load-splitting)
On link-loss, reconverge high-prio, block low-prio
52
Src
Rcv
Rcv
Rcv
Headend LSR

## Slide 12: MSR6 Requirements for Live-Live Protection
Live-Live—Spatial Separation
Two separate paths through network; can engineer manually (or with RSVP-TE P2MP )
Use of two topologies (MTR)- 2 ISIS MT ??
“Naturally” diverse/split networks work well (SP cores, likely access networks too), especially with ECMP
Target to provide “zero loss” by merging copies based on sequence number  Similar to DETNET Concept
Live-Live—Temporal Separation
In application device—delay one copy—need to know maximum network outage

## Slide 13: Legacy Infrastructure Content Delivery End-to-end protocol view
Current Content Access technologies
PIM-SSM (S,G) joins
membership
FIOS / Cable / Satellite
Aggregation
PE-AGG
Core (CN)
FBB Home Net
Access
External Network Eg: Content provider
Headend
Video encoder/ multiplexer
First hop router
IGMP:
{Limits}
{Static-fwd} PIM-SSM
PIM-SSM PIM-SSM
L3 Transport options in clouds:
Native: PIM-SSM or MVPN/SSM MPLS: LSM / mLDP RSVP-TE
Content injection:
External, national, regional, local
IGMPv3 (S,G)
Distribution
/ regional
Dis.
Edge Rtr
IGMPv3 SSM
Fixed Broadband all flavors
AN EAN
CPE/
(RG)
FIBER / DOSCIS
Agg Node
/ BNG
RSVP-TE
P2MP
Agg/Distro
Triple Play
Services
Access Node
Contribution
mLDP/TE
Primary Distribution
Voice, Video,
Internet

## Slide 14: MSR6 Requirements Summary
Fast Reroute (FRR) Protection ~50ms.
Engineer separate diverse protected paths
Scalability of multicast distribution trees
Live-Live Protection = Lossless, Zero Delay
Triple Play services

## Slide 15: USA Domestic Operators & SRv6 deployment
Operators understand the benefits of Segment Routing over IPv6 data plane (SRv6), however thus far the deployments have been limited.
Major benefits of SRv6 over SR-MPLS and reasons why USA operators are planning for SRv6 deployments in the future.
Native SRv6 steering capabilities with SRv6 SRH.
IPv6 flow label support RFC 6437 for native ECMP load balancing.
Data Center underlays for NVO overlay is typically “Non MPLS” and most Data Centers are moving quickly towards SRv6 underlay for steering to fabric attached host endpoints for NFV and SFC service chaining.
IPv6 data plane opens up QOS to use DSCP over MPLS EXP classes.
MPLS elimination allows for ubiquitous use cases for SRv6.

## Slide 16: SRv6 Solutions for Multicast
There is no exact solution for Multicast for Segment Routing SRv6
Depending on the requirements, we can choose the best fit from the following options:
Deploy traditional Multicast Solutions
  PIM
  mLDP
  RSVP-TE
  Ingress Replication (IR)
TreeSID – a controller based solution – uses Replication SID
BGP Multicast & BGP Multicast Controller
Bit Index Explicit replication (BIER)
MSR6 (New)