## Slide 1: Solution Overview Stateless Traffic Engineering Multicast or how to stuff a multicast tree into an IPv6 extension header and be able to process it hop-by-hop MSR6 BoF IETF 114 Philadelphia v1.0 07/21/2022 draft-geng-msr6-traffic-engineering-01, draft-geng-msr6-rlb-segment-00, draft-chen-pim-srv6-p2mp-path-06, draft-chen-pim-mrh6-03, draft-eckert-msr6-rbs-00 and draft-cheng-spring-ipv6-msr-design-consideration Operator Waiqiang Cheng, Ysiong Lio (China Mobile), Aijun Wang (China Telecom), Zuangzhuang Qin (China Unicom) Gyan Mishra, Mehmet Toy (Verizon) Vendor Xuesong Geng, Fenkai Li, Zhenbin Li, Rui Meng, Jingrong Xie, Xiuli Zheng Xuesong Zheng (Huawei) Chi Fan (New H3C Technologies), Yanhe Fan (Casa Systems), Lei Liu (Fujitsu), Xufeng Liu (IBM Corporation/Volta) Research Toerless Eckert, Huaimo Chen (Futurewei)

## Slide 2: MSR6 “Traffic Engineering” Architecture Overview
Page
|<--IPv6 header -->|<--Routing header--->|
+------------------+---------------------+--------------------------+
| Next Header = | Next Header | (other extension header) |
|43(Routing header)| | IP multicast packet/data |
| SA=IPv6 Address |Routing Type=TBD(MRH)| |
| DA=IPv6 Address |Tree/Subtree encoded | |
+------------------+---------------------+--------------------------+
|<------- MRH ------->|
CE4
Tree
Traffic
Source
PE2
PE3
PE5
PE4
CE1
P1
P2
P3
PE1
link
PE10
P4
1
2
1
1
5
2
2
1
1
1
2
3
3
3
4
1
1
1
1
1
1
1
2
3
4
PE6
PE7
PE8
5
1
PE9
Controller
TE P2MP Tree
CE2
CE3
CE5
Stateless native IPv6 forwarding across strict and loose hops with replication
With “Tree Engineering” (Steered Tree)
End-to-End (ingres PE to egres PE), CE-CE via usual IPv6 in IPv6 encap
Loose hops for incremental deployment and simpler, optimized trees
New IPv6 Extension Header – MRH encodes the engineered tree (here assuming routing header)
MRH contains TE P2MP Tree
Notes: -

## Slide 3: Why encode a tree ?
Classical unicast TE + multicast TE reasons
  Resource guarantees, avoid unexpected re-route by IGP
    Admission Controller: reserve bandwidth, latency, no-loss, calulate throughput, latency paths
  Network Capacity optimization
    Like Unicast non-ECMP multipath, but also Steiner trees
  Path Diversity (live-live, disjoint failure domains), reduce loss
    Combined with e.g. MoFRR, PREOF on the edge
Better scalability than “flat bitstrings” ?! (counterintuitive !):
  Flat-bitstrings: Packet can address only destinations (BIER) and hops (BIER-TE) that fit into single bitstring
    Need to hard-segment destinations (BIER) and topology (BIER-TE) into different bitstrings during provisioning
  Example: 256 bit long bitstrings, 2048 egres PE in network, and input packet for 8 of those 2048 egres PE
    Flat-bitstrings: requires 8 packets from ingres to egres PE when all 8 egres-PE are in a different Bitstring.
    Well compressed Tree options can always support delivery via one packet
  Relevance: Sparse multicast (few receivers) was day 1 core IP Multicast goal (PIM-Sparse-Mode)
  Initial large scale MSR simulation result available showing significant better than flat-bistring results!
BIER/BIER-TE was built for assumed minimum feasible complexity - 10 years old
  We know current/next gen hardware can do better
  But selecting / optimizing MRH header for processing performance is one key work item !

## Slide 4: Five MSR6 TE Solution Drafts
Page
Too much Detail and each proposal would take more than half this time slot
  Lets focus on commonalities / aspects
But many authors invested lot of work – and hoped to present their work
  Attempt at high level comparison on next slide
  (best understood if you had seen prior side-meeting slides)
Important aspects in each draft:
  Overall MRH header encoding.
  Tree Encoding:
    How to encode vertices (adjacencies of an MSR on the tree):
      bitstring, SID, interface-index,...
    How to link the vertices
    How to (de)serialize the tree
    Local state required on routers for MSR6 packet forwarding: BIFT (e.g.: like in BIER/BIER-TE) – details of BIFT
    or more (e.g.: Topology)
  Processing rules (explicit through pseudo-code or implied by by structure decision)
Notes: -

## Slide 5
Page
4) IPv6 Multicast Source Routing Traffic Engineering (draft-geng-msr6-traffic-engineering-01)
  End.RL (MSR6 Endpoint Replication List) SID for each node on tree
  Arguments in SID: "Replication number“ indicating the number of replications and a “Pointer” pointing to the first child
  Procedure of SID replicates packet for each child and sends copy to root of child
5) RLB (Replication through Local Bitstring) Segment for Multicast Source Routing over IPv6 (draft-geng-msr6-rlb-segment-00)
  End.RLB (Replication through Local Bitstring) SID with LB
  Local Bitstring indicating the links on tree and Pointer.
  LB Segment is a special segment of 128-bits containing the Local Bitstring.
  Procedure of SID replicates packet for link with bit set to 1 and sends copy to next hop
3) Stateless SRv6 Point-to-Multipoint Path (draft-chen-pim-srv6-p2mp-path-06)
  Multicast SIDs for the nodes on tree
  Tree structure in SIDs’ arguments by N-Branches and N-SIDs as “pointer” to start of sub-tree/branch
  Procedure of SID duplicates packet for each branch, and sends copy to next hop
2) Recursive Bitstring Structure (RBS) for Multicast Source Routing over IPv6 (MSR6) (draft-eckert-msr6-rbs-00)
  Not presented in any MRS6 side meeting yet
  MSR6/RBS IPv6 extension header with Tree AND IP multicast destination address
  TE Tree is represented by the adjacencies on the tree
  The adjacencies are encoded by bit positions in bitstrings
  A bit position is local to a node
Stateless Traffic Engineering (TE) Multicast using MRH (draft-chen-pim-mrh6-03)
  IPv6 extension header for TE Multicast is defined
  TE Tree is represented by the links on the tree
  The links are encoded by Link numbers and bitstrings
  A link number is local to a node
  For a portion of tree, a more efficient encoding (bitstring or link #) is used.
Notes: -

## Slide 6: Example merged MRH Header option (and alternatives)
Single New IPv6 Routing Header for MSR
  Else every new MRH option requires separate Routing Type
MSER-Segment:
  IPv6 destination address of packet
  Or else we need another header for native IPv6 multicast with MSR.
MRH Sub-type:
  To support different MRH options
MRH Sub-Type specific data:
  Encoded list of egress MSR routers (BE)
  or steered tree information (TE)
Service Level Parameters (optional)
  Or else we may need another extension header for them
    Easier if per-hop forwarding only needs to look at one header ?!
  Stateless multicast means no-per-flow state, so this may require novel DetNet queuing mechanisms.
  DSCP may not be good enough.
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len | Routing Type | Segments Left |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| MSER-Segment (128 bit IPv6 address) |
| (optional) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
? ?
? Service Level Parameters, e.g.: detnet ?
? TBD, e.g.: latency, queuing parameters ?
? ?
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-
| MRH Sub-Type | MRH Sub-Type specific data |
+-+-+-+-+-+-+-+-+ //
// ... //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
// //
// Optional Type Length Value (TLV) objects (variable) //
// //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 7: More core decision/validation points
RH (Routing Header), single, multiple, and/or DoH / HbH ?
RFC8200 relevant header encoding/processing rules.
  E.g.: minimum per-hop header rewrite (such as Segments-Left)
How to best Encode/Serialize Tree
  For fast processing and best compression of tree
Metrics for evaluation / comparison of proposals
  Simulation results of scale in networks ?
  Processing Pseudocode ?
  Amount of read/writes required into packet header ?
How to make proposal easier comparable ?
  Pseudocode (popular in multicast – PIM, BIER)
  Common forwarding examples ?
  RFC8200 language ?! (specific form of pseudocode)
  RFC8986 language (popular with user relying on SRv6) ?
Which design aspects would 6MAN be happy to be MSR6 responsibility ?
  Ideally we come up with a split responsibility (e.g.: Tree encoding is MSR6).
    Examples: (Ab)use of IPv6 addressing for IPv6 multicast done in mboned – RFC3956. Quite similar!