## Slide 1: Core Use-Case Requirements for MSR6 from operational/developer perspective aka: extracted/summarized from use-cases
IETF114 Philadelphia
v1.1 - 07/21/2022
how to fit 30 years of IP Multicast protocol design, deployment
and multicast app-development experience into too little time and slides
Toerless Eckert (Futurewei USA), tte@cs.fau.de

## Slide 2: Core MSR6 use-case requirements
There is really only one requirement:
  “Simple”(1) , IPv6 integrated(2), “End-to-End”(3), stateless (4), IPv6 multicast(5) for IPv6-only networks (6)
(6) What IPv6 only networks ?
  A: All IPv6 networks that require IPv6 multicast!
  Explained by other drafts/presentations: SP/WAN/Metro native IPv6 (with/without SRv6) (e.g.:IPTV, MVPN), DCN, OTT/Overlays
  IMHO also: Any enterprise, transportation, IoT network (small..large)
    Not considered by current MSR6 drafts – but should be

## Slide 3: Refresh: BIER and IPv6-only networks(6)
BIER RFC8279 (arch) + RFC8296 (header) is new layer ~ L2 / L2.5
  BIER router (BFR) forwarding is not IPv6 forwarding (RFC8200)
  BIER packets are not IPv6 packets (RFC8200)
Now: “One additional multicast forwarding plane for all unicast networks”
  Initially optimized for MPLS: header: label field (BIFT-ID), TC, OAM, signaling, ...
    Also BIER over L2 only, but little/no operator interest / stalled drafts
BIER-WG solution for IPv6 only networks / IPv6 Multicast ?
  Do not build IPv6-only networks !
    draft-ietf-bier-bierin6 draft:
    Run separate BIER hop-by-hop forwarding plane - parallel + overlay
  End-to-end tunnel for IPv6 Multicast over BIER : 2 headers
    BIER header + IPv6 (multicast) Header (so-called BIER flow overlay)
  2. Transit over IPv6-unicast only routers (loose hops) : 3 headers
    IPv6 unicast header (lower) + BIER header + IPv6 (multicast) header
no endorsement,
i have not read the book
i just like the cover

## Slide 4: Simplicity(1), End-to-End(2) Operational / Architectural alignment/integration(2) with IPv6 (unicast)
30 year experience: IP Multicast solutions are most successful when they minimize the additional ecosystem differences / work over the networks unicast solution
  Do not introduce additional unnecessary multicast technology – reuse everything you can
1989: IP/IPv6 Multicast is re-using / extending IP (RFC1112)(2)
  Allowed to re-use or logically amend IP/IPv6 ecosystem components: SDKs/ sockets-API(*), QoS Diffserv/IntServ(RSVP)(*), ACLs(*), any IP L2 encaps(*), IPFIX(*), IPsec(*), ..
  (*) Most of this would all have to be reinvented / duplicated for BIER but not for MSR6.
  Would have put bitstrings into IPv6 addresses if they where long enough (e.g. Cisco drafts in BIER)!
1990th: We tried novel multicast routing (MOSPF, DMVPN, ...)
  Replaced by PIM + unicast routing (OSPF, ISIS, RIP,...) – because: do not re-invent routing for multicast!
200x: IPv4 multicast MVPN solution for MPLS/VPN SP networks – additional forward/control!
  IPv4 Multicast replaced by native MPLS multicast (mLDP/RSVP-TE/P2P)
  PIM/MVPN signaling replaced by BGP/MVPN signaling – because: we want a single protocol!
IMHO: BIER driven by MPLS SP use-cases (MPLS/MVPN). Well aligned/integrated there!
  But not for the wide range of IPv6 networks – end-to-end – into IPv6 applications
  Non-MPLS networks do not want or need an additional BIER ecosystem

## Slide 5: Stateless(4), (1) .. and End-to-End(3)
BIER or native IPv6/MSR6: Scale and Convergence
  Finance / Telemetry / Content distribution / adaptive streaming would require hundreds of thousands of multicast states. Can not create, re-converge, operate!
Native IPv6/MSR6: Operational simplicity (troubleshooting), safety, reliability
  All stateful multicast (IP or MPLS): Applications create (tree) state on routers in the network. No IETF standard multicast circuit beaker / state congestion/control solutions for multicast state. Any bad or attack multicast application can bring down stateful multicast routers
    Unicast state: routing tables - do not grow with traffic, only with topology
  Global MPLS SPs where deploying ingress-replication to avoid Multicast state on P nodes (RFC7988)
    after we invested 10 years in IETF to specify MPLS multicast – Core reason for BIER
Native IPv6/MSR6: Additional new multicast paradigm for applications
  IP Multicast (and SSM): application signaling: flow based – receiver join/leave group/channels
  Only with stateless multicast:
    Sender can DIRECT EVERY PACKET SEPARATELY – Destinations (and Path – with TE model)
    Only way to enable e.g.: adaptive streaming at scale via multicast
  BIER always wanted/wants to explore this. But IMHO NO WAY to get a ubiquitous BIER socket API
    Prior multicast socket extensions took almost 20 years (e.g.: SSM)
    IPv6 extension header API already defined since 2003 (RFC3542) (no BIER API work)

## Slide 6: Result 1: Network centric core MSR6 arch reqs./goals Expressed as Diffs over BIER
For native IPv6 networks
  With or without SRv6: Reuse existing native IPv6, where ever possible
  Common: Core network centric requirements from SP services design (e.g.: MVPN, IPTV).
Native IPv6 source routing hp-by-hop, end-to-end Native IPv6 multicast, hop-by-hop, end-to-end
  Apply RFC8200 rules hop-by-hop – applicable to IPv6 multicast and/or IPv6 source-routing
  Replace only replication/state rules - not part of RFC8200, but PIM
Day 1 support for path steering and Strict + Loose hops
  Best support for incremental adoption
More scalable BE and TE (path steering) modes
  BIER “flat bitstring” scale limitation for large networks – BIER-TE but also BIER!
    See draft-eckert-msr6-rbs for explanations
  BIER-TE had to re-use BIER forwarding plane as much as possible
  Forwarding planes now can do better!
Integrated support for service guarantees beyond best-effort
  Latency, throughput, loss-protection
  E.g.: support for DetNet natively with MSR6 not on top of MPLS/BIER + UDP end-to-end tunnels
Terminology
  BIER: BFR, BFIR, BFER (BIER) -> MSR6: MSR, MSIR, MSER
CE1
MSER2
MSIRa
MSER1
MSRc
R1
MSRg
CE3
CE2
MSRe
MSRb
MSRd
MSRf
MSR6
domain
Sample topology showing need for
non-equal cost path steering and loose-hop support

## Slide 7: Result 2: End-to-End MSR6 architecture reqs./goals “Host based”
Terminology: MH: IPv6/MSR6 Host (or router) with MSR6 Application.
  No MSIR/MSER required
  But easily an add-on in existing network centric architecture deployments
For (use-case examples)
  IPTV Server -> Caches/Streamers in metro SP
  Data-Center IPv6 Multicast (stateless on DCN switches!)
Support for Host is Router
  Eg.: DC Server running all necessary routing (BGP, IGP)
    E.g.: trusted Hypervisor
  Much easier and important for native IPv6 than BIER (IMHO)
Host API for native source-driven multicast
  Eliminates IP Multicast (RFC1112), SSM (RFC3678) API where not ideal for apps
  E.g.: adaptive streaming cache to subscriber (per-packet functionality)
Support for Host is not router
  More novel network<->host signaling to explore (e.g.: PCEP ?)
  Use-cases: IoT (MANET/ROLL ?), Industrial, Enterprise
MH1
MSRi
MSRa
MSRh
MSRc
R1
MSRg
MH3
MH2
MSRe
MSRb
MSRd
MSRf
MSR6
domain

## Slide 8: Summary / Conclusion
Stateless bitstring replication is the best new multicast direction in 40 years
BIER-WG - great stateless intra-SP solution for MPLS networks
  But inferior fit for IPv6 networks and end-to-end applications
  IETF/BIER can-not / should not change any more than necessary of the IPv6 ecosystem
  Want to improve on what we learned from BIER (and its limitations) to get best IPv6 solution.
MSR6: Keep it simple & Make IPv6 Multicast great again!
  Native stateless multicast - for all IPv6 networks
  Stateless IPv6 multicast into applications (DC, industrial, IoT, SP-edge, ...)
  Re-use / share all of BIER that fits!
Stuffed Agenda, No questions now ?!
  But welcoming questions any time after the meeting!
Go Native
Stateless !