## Slide 1: Solution Overview Stateless Traffic Engineering Multicast MSR6 BoF IETF 114 Philadelphia v1.3 07/25/2022 draft-geng-msr6-traffic-engineering-01, draft-geng-msr6-rlb-segment-00, draft-chen-pim-srv6-p2mp-path-06, draft-chen-pim-mrh6-03, draft-eckert-msr6-rbs-00 and draft-cheng-spring-ipv6-msr-design-consideration Operators Weiqiang Cheng, Yisong Liu (China Mobile), Aijun Wang (China Telecom), Zhuangzhuang Qin (China Unicom) Gyan Mishra, Mehmet Toy (Verizon) Vendors Xuesong Geng, Fengkai Li, Zhenbin Li, Rui Meng, Jingrong Xie, Xiuli Zheng (Huawei) Chi Fan (New H3C Technologies), Yanhe Fan (Casa Systems), Lei Liu (Fujitsu), Xufeng Liu (IBM Corporation/Volta) Toerless Eckert, Huaimo Chen (Futurewei) https://github.com/MSR6-community/presentations/blob/main/msr6-bof-chen-te-solution-overview.{pptx,ppt}

## Slide 2: MSR6 “Traffic Engineering” Architecture Overview
Page 2
|<--IPv6 header -->|<--Routing header--->|
+------------------+---------------------+--------------------------+
| Next Header = | Next Header | (other extension header) |
|43(Routing header)| | IP multicast packet/data |
| SA=IPv6 Address |Routing Type=TBD(MRH)| |
| DA=IPv6 Address |Tree/Subtree encoded | |
+------------------+---------------------+--------------------------+
|<------- MRH ------->|
Stateless native IPv6 forwarding across strict and loose hops
  “Engineered Tree”
  End-to-End (ingress PE to egress PE), CE-CE via usual IPv6 in IPv6 encap
  Loose hops for incremental deployment
New IPv6 Extension Header – MRH encodes the tree
MRH contains TE P2MP Tree
CE4
Tree
Traffic
Source
PE2
PE3
PE5
PE4
CE1
P1
P2
P3
PE1
link
PE10
P4
1
2
1
1
5
2
2
1
1
1
2
3
3
3
4
1
1
1
1
1
1
1
2
3
4
PE6
PE7
PE8
5
1
PE9
Controller
TE P2MP Tree
CE2
CE3
CE5
Encoding P2MP Tree into IPv6 Header, packet forwarded along Tree
Here assuming routing header
Notes: -

## Slide 3: Why Encode a Tree ?
Classical unicast TE + multicast TE reasons
  Resource guarantees for QoS
  Network capacity optimization
  Path diversity (live-live) for reducing loss
Better scalability than “flat bitstrings” ?! (counterintuitive !)
  MSR simulation showing significant (~1 order) better!
  Flat-bitstrings: Need to hard-segment destinations and topology into different bitstrings during provisioning
  Relevance: Sparse multicast was day 1 core IP multicast goal
Example:
256 bit long bitstrings, 2048 egress PE in network, and input packet for 8 of those 2048 egres PE
Flat-bitstrings: requires 8 packets from ingress to egress PE when all 8 egress-PE are in a different Bitstring.
Well compressed Tree options can always support delivery via one packet
Page 3

## Slide 4: Five MSR6 TE Solution Drafts
Page 4
Motivation of presentation
  Focus on common important aspects
  Attempt at high level comparison on next slide
  (many authors invested lot of time, hoped to present their work, each proposal with detail would take half slot, best understood if you had seen prior side-meeting slides)
Important aspects in each draft
  Overall MRH header encoding.
  Tree Encoding:
    How to encode vertices/adjacencies: bitstring, SID, interface-index, ...
    How to link the vertices
    How to (de)serialize the tree
    MSR6 packet forwarding table on each node
  Procedure (explicit through pseudo-code or implied by structure decision)
Notes: -

## Slide 5: Five MSR6 TE Solution Drafts (cont.)
Page 5
4) IPv6 Multicast Source Routing Traffic Engineering (draft-geng-msr6-traffic-engineering-01)
  End.RL (MSR6 Endpoint Replication List) SID for each node on tree
  Args in SID: "Replication number“ indicating the number of replications and a “Pointer” pointing to the first child
  Procedure of SID replicates packet for each child and sends copy to root of child
5) RLB (Replication through Local Bitstring) Segment for Multicast Source Routing over IPv6 (draft-geng-msr6-rlb-segment-00)
  End.RLB (Replication through Local Bitstring) SID with LB
  Local Bitstring indicating the links on tree and Pointer.
  LB Segment is a special segment of 128-bits containing the Local Bitstring.
  Procedure of SID replicates packet for link with bit set to 1 and sends copy to next hop
3) Stateless SRv6 Point-to-Multipoint Path (draft-chen-pim-srv6-p2mp-path-06)
  Multicast SIDs for the nodes on tree
  Tree structure in SIDs’ arguments by N-Branches and N-SIDs as “pointer” to start of sub-tree/branch
  Procedure of SID duplicates packet for each branch, and sends copy to next hop
2) Recursive Bitstring Structure (RBS) for Multicast Source Routing over IPv6 (MSR6) (draft-eckert-msr6-rbs-00) [Not presented in any MRS6 side meeting]
  MSR6/RBS IPv6 extension header with Tree AND IP multicast destination address
  TE Tree is represented by the adjacencies on the tree
  The adjacencies are encoded by bit positions in bitstrings
  A bit position is local to a node
Stateless Traffic Engineering (TE) Multicast using MRH (draft-chen-pim-mrh6-03)
  IPv6 extension header for TE Multicast is defined
  TE Tree is represented by the links on the tree
  The links are encoded by Link numbers and bitstrings
  A link number is local to a node
  For a portion of tree, a more efficient encoding (bitstring or link #) is used.
Segment based
Segment Based
Local bitstring
Using
Routing Header
w/ Local bitstring
+ Multicast Dest
+ Link numbers
SRv6 (SRH)
Notes: -

## Slide 6: Example merged MRH Header option (and alternatives)
Page 6
Single New IPv6 Routing Header for MSR
  Or else every new MRH option requires separate Routing Type
MRH Sub-type:
  To support different MRH options
MRH Sub-Type specific data:
  Encoded list of egress MSR routers (BE)
  or steered tree information (TE)
Service Level Parameters (optional)
  Or else may need another extension header for them
    Easier if per-hop forwarding only needs to look at one header ?!
  Stateless multicast means no-per-flow state, so this may require novel DetNet queuing mechanisms.
  DSCP may not be good enough.
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len | Routing Type | Segments Left |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
? ?
? Service Level Parameters, e.g.: detnet ?
? TBD, e.g.: latency, queuing parameters ?
? ?
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MRH Sub-Type | MRH Sub-Type specific data |
+-+-+-+-+-+-+-+-+ //
// ... //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
// //
// Optional Type Length Value (TLV) objects (variable) //
// //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Notes: -

## Slide 7: More core decision/validation points
Page 7
RH (Routing Header), single/multiple, and/or DoH / HbH ?
RFC8200 relevant header encoding/processing rules.
  E.g.: minimum per-hop header rewrite (such as Segments-Left)
How to best Encode/Serialize Tree
  For fast processing and best compression of tree
Metrics for evaluation / comparison of proposals
  Simulation results of scale in networks ?
  Processing Pseudocode ?
  Amount of read/writes into packet header ?
How to make proposal easier comparable ?
  Pseudocode (popular in multicast – PIM, BIER)
  Common forwarding examples ?
  Unified form of pseudocode ?
Which aspects are MSR6’s responsibility (6MAN happy)?
  Ideally split responsibility (e.g., Tree encoding is MSR6’s).
  Examples: Use of IPv6 addressing for IPv6 multicast done in mboned – RFC3956. Quite similar!
Notes: -

## Slide 8: References
More detailed slide decks for individual solutions in
  https://github.com/MSR6-community/presentations/tree/main/te-drafts
  draft-geng-msr6-traffic-engineering
  https://github.com/MSR6-community/presentations/blob/main/te-drafts/msr6-bof-geng-traffic-engineering.pdf
  draft-eckert-msr6-rbs
  https://github.com/MSR6-community/presentations/blob/main/te-drafts/msr6-bof-eckert-rbs.pdf