## Slide 1: Stateless Traffic Engineering Multicast draft-geng-msr6-traffic-engineering-01 draft-geng-msr6-rlb-segment-00 draft-chen-pim-srv6-p2mp-path-06 draft-chen-pim-mrh6-03 draft-eckert-msr6-rbs-00
Page 1
MSR6 BoF IETF 114

## Slide 2: Architecture Overview
Page 2
Ingress (e.g., PE1) encapsulates the packet in IPv6 MRH with tree
The packet is transmitted along tree to egresses. No state in core, Tree in MRH not changed.
Egress (e.g., PE2) decapsulates the packet in a MRH and sends it to next header process
|<--IPv6 header -->|<--Routing header--->|
+------------------+---------------------+--------------------------+
| Next Header = | Next Header | (an extension header) |
|43(Routing header)| | IP multicast packet/data |
| SA=IPv6 Address |Routing Type=TBD(MRH)| |
| DA=IPv6 Address |Tree/Subtree encoded | |
+------------------+---------------------+--------------------------+
|<------- MRH ------->|
CE4
Tree
Traffic
Source
PE2
PE3
PE5
PE4
CE1
P1
P2
P3
PE1
link
PE10
P4
1
2
1
1
5
2
2
1
1
1
2
3
3
3
4
1
1
1
1
1
1
1
2
3
4
PE6
PE7
PE8
5
1
PE9
Controller
TE P2MP Tree
CE2
CE3
CE5
5 solution drafts use IPv6 routing header, called MRH (Multicast/MSR6 Routing Header), for TE Multicast
MRH contains TE P2MP Tree
For multicast packet to be transported by TE P2MP tree,
Notes: -

## Slide 3: Brief on Solution Drafts (1/2)
Page 3
Draft 2
MSR6/RBS IPv6 extension header is defined
TE Tree is represented by the adjacencies on the tree
The adjacencies are encoded by bit positions in bitstrings
A bit position is local to a node
Draft 1
IPv6 extension header for TE Multicast is defined
TE Tree is represented by the links on the tree
The links are encoded by Link numbers and bitstrings
A link number is local to a node
For a portion of tree, a more efficient encoding (bitstring or link #) is used.
Draft list:
Stateless Traffic Engineering (TE) Multicast using MRH (draft-chen-pim-mrh6-03)
Recursive Bitstring Structure (RBS) for Multicast Source Routing over IPv6 (MSR6) (draft-eckert-msr6-rbs-00)
Stateless SRv6 Point-to-Multipoint Path (draft-chen-pim-srv6-p2mp-path-06)
IPv6 Multicast Source Routing Traffic Engineering (draft-geng-msr6-traffic-engineering-01)
RLB (Replication through Local Bitstring) Segment for Multicast Source Routing over IPv6 (draft-geng-msr6-rlb-segment-00)
Notes: -

## Slide 4: Brief on Solution Drafts (2/2)
Page 4
Draft 4
End.RL (MSR6 Endpoint Replication List) SID for each node on tree
Arguments in SID: "Replication number“ indicating the number of replications and a “Pointer” pointing to the first child
Procedure of SID replicates packet for each child and sends copy to root of child
Draft 5
End.RLB (Replication through Local Bitstring) SID with LB
Local Bitstring indicating the links on tree and Pointer.
LB Segment is a special segment of 128-bits containing the Local Bitstring.
Procedure of SID replicates packet for link with bit set to 1 and sends copy to next hop
Draft 3
Multicast SIDs for the nodes on tree
Tree structure in SIDs’ arguments by N-Branches and N-SIDs as “pointer” to start of sub-tree/branch
Procedure of SID duplicates packet for each branch, and sends copy to next hop
Notes: -

## Slide 5: Summary on Solution Drafts
Page 5
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len |RoutinType=TBD1|Version|Flags|b|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| SL (Subtree Left) |nB (# Branches)| Reserved | IPv6
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ MRH (TBD1)
| Tree/Sub-tree encoded by link numbers and bitstrings | for BE
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|<--IPv6 header -->|<-- TBDx header-->|
+------------------+------------------+------------------------+
| Next Header = | Next Header | (an extension header) |
|43(Routing header)| Routing Type = | IP multicast datagram |
| SA=IPv6 Address | TBDx (MRH) | |
| DA=IPv6 Address | SL, SE, Sub-tree | |
+------------------+------------------+------------------------+
|<---- MRH ---->|
IPv6 extension header as MRH used in Draft 1 and 2
Bitstrings used in Draft 1, 2, and 5 for scalability
SIDs for multicast in SRH used in Draft 3, 4 and 5.
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len |RoutinType=TBD2| Segment Left |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Sub-Type = TBD3| RU-Length | RU-Offset .. |S|R|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MSER-Segment (128 bit IPv6 address) | IPv6
: (optional based on S=1) : MRH (TBD2,TBD3)
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ for TE
| RU0L | Recursive Unit 0 (RU0) ... |
+-+-+-+-+-+ (RBS-Address) :
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
A new Routing Type TBD1 for a MRH
A new Routing Type TBD2 for all MRHs, and a new Sub-Type TBD3 for a MRH
MRH in two ways:
A new Routing Type for a MRH
A new routing type for all MRH and a new Sub-Type for a MRH

## Slide 6: Experiments on a Solution
Page 6
Experiments on solution in draft 2 shows
Scalable
Simple
Prototype implemented
easily and
quick
Simulations
done for large scale SP, e.g., 2048 edge/egress routers
Illustrated it is very scalable,
Its efficiency is about one magnitude higher
Notes: -

## Slide 7: Next Steps
Page 7
Converge these TE multicast solutions
MRH
Encoding of Tree
Notes: -

## Slide 8: Next
Comments
Page 8