## Slide 1: MSR6 WG – Solution Overview
IETF114 Philadelphia
v1.0 - 07/14/2022
Toerless Eckert (Futurewei USA), tte@cs.fau.de

## Slide 2: How do we specify MSR6 solutions in the IETF
Assume there is enough support to work on MSR solutions
  because native IPv6 could use better multicast
  Or whichever use-case spurs your interest to collaborate/contribute!
There would surely be already a single IETF WG that we could just bring the work to, right ?
  There are already so many working groups, just pick the right one!

## Slide 3: Network centric (core) MSR6 architecture
Terminology:
  MSR: MSR6/IPv6 Router , SP P node, ~ BIER BFR
  MSIR: MSR6/IPv6 Ingres Router, SP ingres PE node, ~ BIER BFIR
  MSER: MSR6/IPv6 Egres Router, SP egres PE node, ~ BIER BFER
  R: IPv6 router without MSR6 support
  MSR domain: MSIR ... MSER
Strict and loose MSR6 hops (loose: MSR6-R1-MSR3)
Shortest path and steered path (MSIR1-MSR4-MSR5-MSR1-MSER1)
IPv6 packet with MSR6 routing header (MRH) from MSIR to MSER
  BE MRH option: header indicates only set of MSER for packet
  TE (“traffic engineering”): header indicates MSER and intermediate MSR hops
Services
  CE – CE: IPv6 multicast
    CE-MSER/MSIR: IPv6 multicast (MLD signaling, if CE are routers then also PIM
    IPv6 into IPv6 encap/decap on MSIR/MSER, e.g.: MVPN [I/S]PMSI mapping
    Mapping onto specific MSR domain service options
    E.g: DetNet – latency, throughput guarantees, path diversity PEROF on MSIR/MSER.
CE1
MSER2
MSIR1
MSER1
MSR1
R1
MSR3
CE3
CE2
MSR2
MSR4
MSR5
MSR6
MSR6
domain

## Slide 4: End-to-End MSR6 architecture “Host based”
Terminology:
  MH: MSR6/IPv6 Host (or router) with Application. No MSIR/MSER used.
  Can be option in existing network centric architecture
Use-case Example:
  IPTV Server -> Caches/Streamers in metro SP
  Data-Center IPv6 Multicast (stateless on DCN switches!)
Host is router
  DC-Server but running all necessary routing (BGP, IGP)
  Common option in DCN servers now E.g.: trusted in Hypervisor, not third-party container/VM application side!)
Host is not router
  Lightweight non-SP/DCN use cases ?! IoT (MANET/ROLL ?), Industrial,
  E.g.: New PCE<->Host signaling to determine MSH to use
Host is or is not router (most exciting option):
  Native MSR6 application service: No IPv6 multicast
MH1
MSER9
MSR7
MSR8
MSR1
R1
MSR3
MH3
MH2
MSR2
MSR4
MSR5
MSR6
MSR6
domain

## Slide 5: Architecture – further core points
Control Plane architecture – various options
  IGP-only for BE. Even for TE mode, e.g.: MSIR based PCE (e.g.: with LSP IGP)
  Central PCE based for TE mode.
Native MSR6 service
  Significant application benefits, e.g.: adaptive streaming
  May require abstract API specification (e.g.: like MLDv2 API or TAPS for transport)
TBD: Integration / support for DetNet
  If/when IPv6 unicast agrees on extension header for DetNet (currently only MPLS based)
  (almost) Strict path usually required to guarantee latency, throughput, loss -> TE mode
  May want to integrate TBD native DetNet IPv6 extension header elements into MRH
    Especially when requiring per-hop DetNet functionality – no multiple routing headers!
Integration / Use in existing unicast architectures
  (IMHO): Not mandatory to deploy MSR6, but part of alignment if network uses it
  SRv6, ROLL/RPL ...

## Slide 6: Core dependency (6man): MSR6 Routing Header (MRH)
New IPv6 Routing Header
MRH Sub-type:
  support different encoded
    BE (list of MSER)
    TE (steered tree) information.
IPv6 Multicast support:
  Need to carry IPv6 destination address to support the native IPv6 multicast model / existing MVPN signaling for IPv6
  In IPv6 source routing, IPv6 destination address is rewritten on every source routed hop with address derived from routing header, derived from MRH Sub-Type specific data
  Current spec: RBS draft has it as part of RBS Sub-type data. But ideally part of common MRH header
  Not included/used when mapping services from BIER (which may or may not be desired in IPv6 control plane solution).
TLV:
  Same/similar type of TLV functionality as SRv6 SRH
DetNet integration ?
  TBD
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len | Routing Type | Segments Left |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| MSER-Segment (128 bit IPv6 address) |
| (optional) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
? ?
? DetNet parameters ? ?
? (TBD, e.g.: latency, queuing parameters) ?
? ?
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-
| MRH Sub-Type | MRH Sub-Type specific data |
+-+-+-+-+-+-+-+-+ //
// ... //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
// //
// Optional Type Length Value (TLV) objects (variable) //
// //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+