## Slide 1: MSR6 BE Solution
Yisong Liu (China Mobile)
Jingrong Xie (Huawei Technologies)
Xuesong Geng (Huawei Technologies)
Mengxiao Chen (New H3C Technologies)
draft-lx-msr6-rgb-segment-03 & draft-xl-msr6-source-segment-02
IETF-114 Meeting, July 2022

## Slide 2: MSR6 BE
2
MSR6 BE Solution
IPv6 Unicast
IPv6 Unicast
Root Node
IPv6 Ext Hdr
Info of Leaf Node 1 & 2
Multicast payload
IPv6
DA = Next Replication Node
Replication Node
Leaf Node 1
Leaf Node 2
IPv6 Ext Hdr
Info of Leaf Node 1
Multicast payload
IPv6 Hdr
DA = Leaf Node 1
IPv6 Ext Hdr
Info of Leaf Node 2
Multicast payload
IPv6 Hdr
DA = Leaf Node 2
Transit Node
IPv6 Unicast
Root node indicates the target leaf nodes in the packet.
Replication nodes replicate packets according to the leaf node information in the incoming packet.
The packets are transferred as IPv6 unicast along the shortest path. Transit Nodes are MSR6 un-aware.

## Slide 3: RGB Segment & RGB Option
IPv6 Header with RGB Segment as Destination Address, indicating the next MSR6 Replication Endpoints in an MSR domain.
IPv6 Destination Options Header with RGB Option, carrying global bitstring of egress nodes and reusing BIER mechanism.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Next Header | Hdr Ext Len | Option Type | Option Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ RGB Option Data ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+----------------+------------------+----------------------+
| IPv6 header | IPv6 DO Header | Client Multicast |
|DA = RGB Segment| with RGB Option | Packet or Upper |
| | | Layer Encapsulations|
| Next Hdr = 60 | Nxt Hdr = X | |
+----------------+------------------+----------------------+
| | |
|<---------MSR6 BE header---------->|<--MSR6 BE payload--->|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| BIFT-id | Rsv | TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Rsv | Ver | BSL | Entropy |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|OAM|Rsv| DSCP | Rsv |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| BitString (first 32 bits) ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ BitString (last 32 bits) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
End.RGB Behavior:
1. Lookup BIFT(Bit Index Forwarding Table, RFC8279) based on the bitstring inside the RGB Option Data.
2. Forward the packet via the matched entry in the BIFT.
MSR6 BE Solution

## Slide 4: Packet Processing Procedure
A
B
D
C
E
Ingress Node
(Root Node)
Replication Endpoint
Transit Node
Egress Node
(Leaf Node)
Egress Node
(Leaf Node)
BFR-id=2
BFR-id=3
Transfer as Unicast
Replicate
Replicate
IPv6 Hdr
DA=End.RGB-B
DOH
RGB.BitStr=0110
Payload
IPv6 Hdr
DA=End.RGB-D
DOH
RGB.BitStr=0010
Payload
IPv6 Hdr
DA=End.RGB-E
DOH
RGB.BitStr=0100
Payload
Ingress Node: A host originating the MSR6 packet, or a router encapsulating the customer packet in an MSR6 header.
Replication Endpoint: Get an RGB Segment instruction by FIB lookup, and process the RGB Option in DOH. Look up the corresponding BITF, replicate the packet, update the bitstring and DA in each replicated, and forward to the next MSR6 Replication Endpoints.
Transit Node: Transit the packet as a unicast IPv6 packet. Can be MSR6-unaware.
Egress Node: If it is the edge of a network domain, send the packet to the multicast flow overlay; If it is the host supposed to receive the packet, send the packet to the upper layer.
MSR6 BE Solution

## Slide 5: Source Segment Concept
SRv6-SID as Destination Address:
  [RFC8402] The active segment is indicated by the Destination Address (DA) of the packet.
SRv6-SID as Source Address in the existing work:
  [RFC8986 & RFC9259] The active segment (SRv6-SID indicated by the DA) can be PING.
  [RFC4433] Requires that the IPv6 address in the DA of a Ping request (the SRv6-SID above) as SOURCE Address of the Echo Reply Packet.
draft-xl-msr6-source-segment:
  Uses MSR6 SID as SOURCE Address of an IPv6-encapsulated multicast packet.
  The MSR6 Segment represented by such MSR6 SID is defined as “Source Segment” .
MSR6 BE Solution

## Slide 6: Source Segment for MSR6 MVPN service
In the multicast service, packet is replicated along the tree towards a set of leaf nodes. MVPN information could be encapsulated in the Source Segment carried in the IPv6 source address.
Source Segment is distributed by the root node and the function is executed by the leaf nodes.
Source Segment is not changed when the packet is replicated and forwarded along the P2MP path.
Not only for MSR6 MVPN, Source Segment can also be used for MVPN based on other multicast technologies, e.g., BIER, PIM, SR-P2MP.
Src.DT4 | Source address for decapsulation and IPv4 table lookup
Src.DT6 | Source address for decapsulation and IPv6 table lookup
Src.DT46 | Source address for decapsulation and IP table lookup
Src.DT2 | Source address for decapsulation and L2 table lookup
MSR6 BE Solution
Using source segment could bring the following benefits:
Extend the programming space in IPv6 header.
Provide semantic for source address.
Facilitates security management inside the limited domain.
Source segment behaviors:

## Slide 7: Encapsulation of Source Segment and RGB Segment for MSR6 MVPN
Use Source Segment in the IPv6 source address for identifying a VRF in IPv6 multicast source routing.
Use RGB Segment in the IPv6 destination address for indicating the next Replication Endpoint.
Use RGB Option in the DOH for carrying the global bitstring of egress nodes.
MSR6 BE Solution
PE3
id=3
PE2
id=2
Multicast source
IPv4/6 Hdr
SA:X,DA:mcastX
payload
P
MSR6 Domain
IPv6 Hdr(Outer):
SA: PE1 (Src.DTx),
DA: PE2/PE3 (End.RGB)
Dest Opt Hdr:
Bitstring: 0010/0100
IPv4/6 Hdr(inner):
SA: X, DA: mcastX
Payload
IPv6 Header
RGB
In IPv6 DoH
IPv6 Hdr(Outer):
SA: PE1 (Src.DTx),
DA: P (End.RGB)
Dest Opt Hdr:
Bitstring: 0110
IPv4/6 Hdr(inner):
SA: X, DA: mcastX
Payload
IPv6 SA
VPN or public network multicast service with Scr.DTx
Public or private IPv4/6 multicast packets
IPv6 DA
Indicate next MSR6 Replication Endpoint
PE1
IPv4/6 Hdr:
SA: X, DA: mcastX
Payload
RGB DoH Option
BIER Forwarding may be re-used

## Slide 8: Next Steps
Revise the draft according to feedbacks
  Comment by Toerless: removing unnecessary fields in the RGB Option.
  Other MSR6 BE solution, e.g., draft-chen-pim-be-mrh: discussing with the authors for coordination between different solutions.
Any questions or comments are Welcomed
MSR6 BE Solution

## Slide 9: Thanks